Approval Sheet

| 客户名称/cu stomer name | 领跑能源 |
| --- | --- |
| 产品型号/Model | JP-KP-PE5A PCM |
| 产品规格/Specification | LФ17*0.8mm MAX |
| 主要器件 Main configuration | IC: 精工/S8261G2J MOS:PE5AODZ*4 |
| PCB工艺/PCB | 双层，普通金，绿油，ROHS |
| Document NO. | KEE-PMC |
| 版本/ Rev | V1.0 |
| 部门 Department | 编写(R&D) Registered | 审核 (R&D) Checked | 复核 (Quality) Deliberation | 批准(R&D) Approved |
| 签名/Sign | 韩开年 |  |  | 周雪军 |
| 日期/DATE | 2017.10.26 |  |  | 2017.10.28 |
| 客户确认 Customer Approve |
| 部门 Department | R&D | Quality | Approved |
| 签名/Sign |  |  |  |
| 日期/DATE |  |  |  |
| 文件有效期限 Approved date | 有限期限为1年 Period of validity 1 year |

在文件到期前一个月如果双方都对此文件都没有异议，此文件将自动延续有效期1年

If both sides have no dissidence in one month before the maturity of the Approved. It will be

considered valid automatically for a one year period.

| 公司名称 The name of company | 深圳市静平电子有限公司 SHENZHENKEE ELECTRONIC TECHNOLOGY CO.,LTD | 电话 TEL | 0755-29791802 |
| --- | --- | --- | --- |
| 公司地址 Address | 深圳市宝安区40区安乐工业园B栋 Area40Baoan Industrial Park,BuildingB Shenzhen GUANGDONG, CHINA. |

1.产品变更履历/Product Modified Record List

| 产品变更履历/ Product Modified Record List |
| --- |
| 日期/ Date | 变更点描述/ Problem and Solution | 责任人/ Principal |
| 2017.10.26 | 1.新开发 | 韩开年 | VERSION:V1.0 |

2.产品规格/ Produce Specification

|  | 技术规范 | Rev | 00 |
| --- | --- | --- | --- |
|  | TECHNICAL SPECIFICATION FOR APPROVAL | Date | 2017.10.26 |
|  |  | Page | 1 |

| No | Item | Condition | Specification |
| --- | --- | --- | --- |
| 1 | 输入电压/input Voltage | B+/B-间输入电压/input Voltage B+ to B- | 1.5~+5V |
| 2 | 过充电 Overcharge | 保护电压/Detection voltage | 4.325±0.025V |
| 3 |  | 恢复电压/ Release voltage | 4.075±0.05V |
| 4 |  | 保护延迟时间/ Detection delay time | 960～1400 mS |
| 5 | 过放电 Over discharge | 保护电压/Detection voltage | 2.5±0.05V |
| 6 |  | 恢复电压/ Release voltage | 2.9±0.1V |
| 7 |  | 保护延迟时间/ Detection delay time | 115～173ms |
| 8 | 放电过流 Over discharge current | 放电过流保护电流/Over current | 38-55A |
|  |  | 放电过流保护延时/delay time | 7～12ms |
| 9 | 充电过流 Over charge current | 充电过流保护电流/Over current | / |
|  |  | 充电过流保护延时/delay time | / |
| 10 | 短路保护 | 短路保护延时/ Short detection delay time | 220～380us |
| 11 |  | 恢复条件/Release Conditions | 断开负载/Cut off load |
| 12 | 自耗电 Normal current consumption | 工作状态自耗电 Normal current consumption of PCM | MAX:10uA |
|  |  | 静态自耗电 | MAX:0.1uA |
| 13 | OV充电/0V charger | 是否允许0V充电/allowed 0V change | YES |
| 14 | 建议工作条件 Suggest working conditions | 建议持续充/放电电流 max continuous charge/discharge current | 10A |
| 15 |  | 建议工作温度/suggest working temperature | -20℃～+60℃ |
| 16 |  | PCM内阻/IR of PCM | ≤25mΩ |
| 17 | NTC阻值 | NTC阻值(20~30)℃ | / |
| 18 | PTC阻值 | PTC内阻值 | / |
| 19 | PCM尺寸 The size of final PCM | 圆板/The length of final PCM | Ф15.8±0.15mm |
| 20 |  | 圆板/The width of final PCM | / |
| 21 |  | 厚度/The thickness of final PCM | 0.8+0.1mm |
| 22 | 外观 Appearance | 没有元器件的破损/Nothing part deflection 所有焊点良好/The status of solder is all right PCM 没有翘曲/ PCM will not crook 符合静平电子的出货外观标准/ Settle for LTW Module appearance standard |
| 23 | 可靠性测试Reliability test | ESD 测试：接触 4KV 空气 8KV / ESD test ：connect 4KV Air 8K |
| 24 | 镍片推力 | 推力≥30N |

3. Part List

| 贴片图/SMT drawing |
| --- |
| 贴片位号Location | 物料名称Description | 型号/规格 Specification | 尺寸/封装 Size | 数量 Qty | 供应商 Vendor | 环境 ROHS | 备注 Remark |
| U1 | IC | S8261G2J | SOT-23-6 | 1 | SEIKO | ROHS |  |
| U2,U3,U4,U5 | MOS | PE5AODZ | PDFN 3x3S | 4 | UNIKC | ROHS |  |  |  |  |  |  |  |  |
| R1 | 贴片电阻 | RP-470R-5% | 0603 | 1 | WALSIN | ROHS |  |
| R2 | 贴片电阻 | RP-2K-5% | 0603 | 1 | WALSIN | ROHS |  |
| C1 | 贴片电容 | 0.1uf,±20%,Y5V,25V | 0603 | 1 | SKYWELLY | ROHS |  |
|  | PCB | JP-KP-PE5A 镀金0.1um，绿油 | Ф17*0.8mm | 1 | MEIYADI | ROHS |  |

4. 图纸/Drawing

4.1 电气原理图/Circuit Drawing

4.2 PCM结构图纸/Mechanical Drawing

5. 走线图/Layout

1. 顶层丝印                           2.顶层焊盘

- 顶层线路                              4. 底层线路

6. 包装、运输指引/ Packing and shipping guide Packing

6.1包装

Packing

将拼板用气泡膜包好，放入防静电袋中，上下各放一层隔板，再放入小箱中，四小箱装入一大箱中。

Product packed by ESD Air bubble film , put into ESD packer ,insert 2 piece of clapboard, and then put into  small box and one big box contain 4 small boxes

6.2运输

Shipping

用快递或派专人送货到对方仓库。

Delivery to your storehouse by express or our deliveryman.

运输过程中，应注意防潮、防湿，避免挤压、碰撞等，以免保护板变形。

Pls avoid moisture , humidity, extrusion、hitting so as to prevent PCM damaged during shipping.