SPECIFICATION

OF

#### PCM Type: XZD-1755-1S（G2J）

KEEPPOWER TECHNOLOGY CO., LIMITED

Add：Bldg C, Hepingang High Tech Park, LongGang, Shenzhen 518129, China

Tel: +86 755 8930 9658 Fax: +86 755 8930 9659

www.keeppower.com.cm

1. Scope

The specification is applied to the protection of one-cell lithium-ion battery pack from overcharge, over-discharge and excess current.

2. Specification

2.1 Name: XZD-1755-1S-2MOS

2.2 Circuit Schematic Diagram:  Refer to Figure 1.

2.3 PCB Form Diagram: Refer to Figure 2.

2.4 PCB Material: FR4 (17.5*17.5mm)

2.5PCB Size Form Diagram Refer to Figure 3

2.6PCB Connect Form Diagram Refer to Figure 4

3. Electric Characteristics (Ta=25℃)

3.1 Overcharge detection voltage(VCU):             4.325±0.05V

3.2 Overcharge detection delay time:               1.0±0.5 S

3.3 Overcharge release voltage:                   4.075±0.05V

3.4 Under-discharge detection voltage(VDD):         3.0±0.10V

3.5 Under-discharge detection delay time:           1.0±0.5 S

3.6 Under-discharge release voltage:               2.5±0.1V

3.7 Excess current threshold (IEC):                         8-10A

3.8 Maximum Continuous Current                 7-8A

3.9 Short detection delay time:                    MAX.18mS

3.10 Supply current （V cell=3.5V） :             MAX.10μA

3.11 Standby current（V cell=1.8v） :             MAX. 1uA

3.12 PCB total resister:                          MAX. 30mΩ

4. Function Description

4.1 The PCB is applied to protection of  ONE cells lithium-ion battery pack, which is set

according to requirement of customer.

4.2 Overcharge protection：

The overcharge protection operates when voltage of cell more than VCU with charger at P+ and P-, then charge will be stopped and discharge will be allowed.

4.3 Over-discharge protection：

The over-discharge protection operates when voltage of cell more than VDD with load at P+ and P-, then discharge will be stopped and charge will be allowed.

4.4 Excess current protection:

The Excess current protection operates when current more than IEC with load at P+ and P-, then discharge will be stopped and charge will be allowed.

5. Parts List

| Name | Quantity | Reference | Part |
| --- | --- | --- | --- |
| CAP | 1 | C1 | 104 |
| RES | 1 | R1, | 471 |
| RES | 1 | R2 | 202 |
| IC | 1 | U1 | S-8261ABJMD |
| MOSFET | 2 | U2 | 8822 |

##### Figure 1 Schematic Diagram

# Figure 2 PCB Form Diagram

# Figure 3 PCB Size Form Diagram

# Figure 4 PCB Connect Form Diagram

| PIN | function |
| --- | --- |
| B+ | Connect Cell + |
| B- | Connect Cell - |
| P- | Connect charger - or load - |

# Figure 5 Picture

# Text boxes

| Approved by | Checked by | Prepared by |
| --- | --- | --- |
| Bin Zhao | Xiaopeng Chen | Lujin An |