SPECIFICATION

OF

#### PCM Type: XZD-2004-B

KEEPPOWER TECHNOLOGY CO., LIMITED

Add：Bldg C, Hepingang High Tech Park, LongGang, Shenzhen 518129, China

Tel: +86 755 8930 9658 Fax: +86 755 8930 9659

www.keeppower.com.cm

1. Scope

The specification is applied to the protection of two-cells lithium-ion battery pack from overcharge, over-discharge and excess current.

2. Specification

2.1 Name: XZD-2004-B

2.2 Circuit Schematic Diagram:  Refer to Figure 1.

2.3 PCB Form Diagram: Refer to Figure 2.

2.4 PCB Material: FR4 (55mmx4.2mm)

3. Electric Characteristics (Ta=25℃)

3.1 Overcharge detection voltage(VCU):             4.35±0.025V

3.2 Overcharge detection delay time:               1.0±0.5 S

3.3 Overcharge release voltage:                   4.15±0.05V

3.4 Under-discharge detection voltage(VDD):         2.30±0.08V

3.5 Under-discharge detection delay time:           1.0±0.5 S

3.6 Under-discharge release voltage:               3.0±0.1V

3.7 Excess current threshold (IEC):                         4A-5A

3.8 Maximum Continuous Current                 2-3A

3.9 Short detection delay time:                    MAX.10mS

3.10 Supply current （V cell=3.5V） :             MAX.10μA

3.11 Standby current（V cell=1.8v） :             MAX. 1uA

3.12 PCB total resister:                          MAX. 50mΩ

4. Function Description

4.1 The PCB is applied to protection of two cells lithium-ion battery pack, which is set

according to requirement of customer.

4.2 Overcharge protection：

The overcharge protection operates when voltage of cell more than VCU with charger at P+ and P-, then charge will be stopped and discharge will be allowed.

4.3 Over-discharge protection：

The over-discharge protection operates when voltage of cell more than VDD with load at P+ and P-, then discharge will be stopped and charge will be allowed.

4.4 Excess current protection:

The Excess current protection operates when current more than IEC with load at P+ and P-, then discharge will be stopped and charge will be allowed.

5. Parts List

| Name | Quantity | Reference | Part |
| --- | --- | --- | --- |
| CAP | 3 | C1, C2，C3 | 104 |
| RES | 1 | R5 | 4.7M |
| RES | 3 | R1,R2,R3,R4 | 1K |
| RES | 1 | R6 | 10K/NTC |
| IC | 1 | U1 | R5460 |
| MOSFET | 1 | U9 | 8814 |

##### Figure 1 Schematic Diagram

# Figure 2 PCB Form Diagram

# Figure 3 PCB Size Form Diagram

# Figure 4 PCB Connect Form Diagram

# Text boxes

| Approved by | Checked by | Prepared by |
| --- | --- | --- |
| David Zhang | Qingming Dai | Lujin An |