SPECIFICATION

OF

#### PCM Type: XZD-3S1550-V3

KEEPPOWER TECHNOLOGY CO., LIMITED

Add：Bldg C, Hepingang High Tech Park, LongGang, Shenzhen 518129, China

Tel: +86 755 8930 9658 Fax: +86 755 8930 9659

www.keeppower.com.cm

1. Scope

The specification is applied to the protection of three-cell lithium-ion battery pack from overcharge, over-discharge and excess current.

2. Specification

2.1 Name: XZD-3S1550-V1  （4MOS）

2.2 Circuit Schematic Diagram:  Refer to Figure 1.

2.3 PCB Form Diagram: Refer to Figure 2.

2.4 PCB Material: FR4 (50.0mmx15.0mm)

2.5PCB Size Form Diagram Refer to Figure 3

2.6PCB Connect Form Diagram Refer to Figure 4

3. Electric Characteristics (Ta=25℃)

3.1 Overcharge detection voltage(VCU):             4.275±0.05V

3.2 Overcharge detection delay time:               1.0±0.5m S

3.3 Overcharge release voltage:                   4.075±0.05V

3.4 Under-discharge detection voltage(VDD):         2.30±0.10V

3.5 Under-discharge detection delay time:           1.0±0.5 mS

3.6 Under-discharge release voltage:               2.70±0.1V

3.7 Excess current threshold (IEC):                         10A-18A

3.8 Maximum Continuous Current                 5-6A

3.9 Short detection delay time:                    MAX.18mS

3.10 Supply current （V cell=3.5V） :             MAX.10μA

3.11 Standby current（V cell=1.8v） :             MAX. 1uA

3.12 PCB total resister:                          MAX. 55mΩ

4. Function Description

4.1 The PCB is applied to protection of three-cells lithium-ion battery pack, which is set according to requirement of customer.

4.2 Overcharge protection：

The overcharge protection operates when voltage of cell more than VCU with charger at P+ and P-, then charge will be stopped and discharge will be allowed.

4.3 Over-discharge protection：

The over-discharge protection operates when voltage of cell more than VDD with load at P+ and P-, then discharge will be stopped and charge will be allowed.

4.4 Excess current protection:

The Excess current protection operates when current more than IEC with load at P+ and P-, then discharge will be stopped and charge will be allowed.

5. Parts List

| Name | Quantity | Reference | Part |
| --- | --- | --- | --- |
| CAP | 6 | C1,C2, C3, C4, C5, C7 | 0.1uf /0603 |
| RES | 2 | R1, R3 | 5.1kΩ±5%/0603 |
| RES | 1 | R2 | 1MΩ±5%/0603 |
| RES | 6 | R5, R6,R7,R8,R9,R10，R11 | 1kΩ±5%/063 |
| RES | 1 | R117 | 51Ω±5%/0805 |
| RES | 2 | R14,R？ | 10mΩ±5%/1206 |
| IC | 1 | U1 | S-8254-AAG |
| MOSFET | 4 | PQ1,PQ2, PQ3,PQ4 | AO4407 |
| PCB |  |  | 50*15mm |

##### Figure 1 Schematic Diagram

# Figure 2 PCB Form Diagram

# Figure 3 PCB Size Form Diagram

# Figure 4 PCB Connect Form Diagram

# Text boxes

| Approved by | Checked by | Prepared by |
| --- | --- | --- |
|  | Xiaopeng Chen | Lujin An |